LU Library Utility

              LU is a utility to manipulate "LBR" files generated 
         by the PC-DOS utility of the same name.  The most common 
         use is to  pack a group  of related files  into a single 
         .LBR file, for modem transfers or for archiving. 

              LU  or an equivelant program is usually required to 
         "unpack"  the   software  packages   available  on   the 
         Chesapeake Remote Bulletin Board System. 

              .LBR  files are  special files  generated by LU (or 
         whatever)  that  contain  one  or  more DOS files  and a 
         simple  directory.  Whenever   an  existing  library  is 
         changed (files  changed or deleted) the library requires 
         "reorganizing".  More on this below. 

              LU operation is quite simple.  There are only a few 
         commands.  Each is described  below, and a quick summary 
         can be obtained by running LU like so: 

                   LU <cr> 


                              OPERATING LU

              LU commands are entered  on the command line  after 
         the  program  name.   You  must  ALWAYS  enter a command 
         letter, below, and the name of an LBR file, followed  by 
         file names, if needed: 

            LU <command> <lbr file name> { <optional filenames> } 

                   For example:   LU T FILE.LBR 

              Lists  all the files contained  within the LBR file 
              FILE.LBR. 


                          L U    C O M M A N D S

              All LU commands  are a single letter.  Only one can 
         be entered at a time. 

         A - UNPACK all files from the library.  This is the same 
              as  the E  (extract) command,  followed by  all the 
              file names. This is much easier if all  you want to 
              do is remove all the files. 

         D -  DELETE a file.  The just marks the file  within the 
              library as  "deleted".  The  library file  will NOT 
              change  in  size;  it  does  not  remove  the  data 
              contained  by  the   file.   See  "reorganization", 
              below. 


         E -  EXTRACT a file from the library.  The file(s) to be 
              extracted  are  entered  after  the  LBR file name.  
              Each  file will be extracted,  and copied to a disk 
              file of the same name. 

         L  -  LIST  all files  contained in  the LBR file.  Each 
              filename is listed, along with the size of the file 
              in  bytes, and  its starting  offset within the LBR 
              file.  (The offset  is pretty useless  information, 
              but there it is.) 

         R  -   REORGANIZE  the  library.   All  free space (from 
              deleted files, or existing files that were Updated) 
              is  freed up,  and the  LBR file  generally becomes 
              smaller. Should  be used  after a  Delete or Update 
              command.    Creates   a   temporary   file   called 
              LU$$$$$$.TMP, therfore you should not use this file 
              name elsewhere. 

         T -  Same as L. 

         U -  UPDATE a library.  This is ALSO used  to CREATE NEW 
              LIBRARIES.  File  name(s) are entered after the LBR 
              file name,  and each file is  added to the library.  
              Any file  of the same  name already in  the library 
              will be deleted first, otherwise just added. Please 
              read about reorganizing, below. 

              If the library file does not  exist (creating a new 
         one) then you are asked for the  number of new slots for 
         the library. "Slots" means  the maximum number of  files 
         that the LBR file can contain.  The number you  enter is 
         rounded up to the next highest multiple of four; this is 
         just a peculiarity  of the LBR file  structure.  It does 
         not hurt  anything.  After  the new  library is created, 
         any specified files are added to it. 

         
                       R E O R G A N I Z I N G

              The structure of an .LBR file (described in  detail 
         below)  is very simple. Because of its simplicity, files 
         that are  deleted or changed still  consume space within 
         the  LBR  file,  which  must  be "squeezed" whenever the 
         library is changed. 

              Deleteing  a   file  merely   marks  the   file  as 
         "deleted"; it does  not remove the data contained in the 
         LBR  file.  Updated  files  are  deleted first, and also 
         consume   space.   Therefore,   the   library   must  be 
         reorganized. This  consists of  creating a  new library, 
         and copying the active files to it, dropping out all the 
         deleted or changed data. 

              The rule is:  reorganize after deleting  a file, or 
         updating  a file  that already  existed.  If the library 
         runs  out  of  slots,  and  you  want to add more files, 
         reorganize and specify a larger number of slots. You can 
         then add to the library. 

              Reorganizing never does any harm, in any case. 


               L B R    F I L E    S T R U C T U R E

              The LBR file is a disk file  that contains a simple 
         directory, followed  by all  the data  contained in  the 
         files.  New files are  added to the end of the LBR file, 
         and  the  directory  entry  for  each file points to the 
         data, and contains its length. Each directory entry is: 

              00:file status (0= active, FF= deleted, FE= unused) 
              01:11 character filename (FCB format) 
              12:16 bit offset to start of data (in sectors) 
              14:16 bit data length (in sectors) 
              16:16 bytes of filler 

              Since  the original  program was  written in BDS C, 
         all offsets  and lengths are in  multiples of 128 bytes, 
         the CP/M "sector  size".  LU multiplies these  values by 
         128 before  using. (Also, all file  sizes are rounded up 
         to the nearest 128 bytes.) 

              The  offset  is  the  location  of the data for the 
         file,  relative to the start of  the LBR file. The first 
         directory  entry is the  directory itself.  The filename 
         is always blank, the offset is not used,  and the length 
         is the length  of the directory.  Since the length  is a 
         multiple of 128, LU rounds  up the number of slots  when 
         creating  a new  .LBR file  to a  multiple of  four. (32 
         bytes per entry  * 4 == 128). 


                         P E C U L I A R I T I E S 

              There  are  only  two  peculiarities  (nice  way of 
         saying  "bugs")  that  I   know  of: 

              1.   Filenames  without  extentions,  like   "FILE" 
              instead of "FILE.EXT"  should be entered  without a 
              dot.  Entering  with a  dot will  cause "NOT FOUND" 
              errors  to  be  generated.   (I.e.  use  "FILE" not 
              "FILE.". 

              2.   Not  really a  bug, but  a side  effect of the 
              original  design: all  files are  rounded up to the 
              nearest 128 bytes.  This  does not matter for  most 
              files, but  some, like spreadsheet  files, will not 
              work  unless  the  size  is  exactly right.  LU (or 
              equivalent) cannot be used with such files. 

         Try it and see what happens!